File ‘dtfs_ex.m’

% A script to demonstrate the Discrete-Time Fourier Series

% for a sawtooth with period N = 3.

% Define the periodic wave in the sample domain.

% Let x(n) be the samples of the wave.  Let xp be a finite set of

% samples that defines the fundamental period of sample values from

% Sample number zero to sample number N-1 where N is the period.

xp = [0, 1, 2];               % The fundamental period of x(n)

N  = length(xp);              % The fundamental period

% Now make a plot from sample number Nmin to sample number Nmax

Nmin = -4;

Nmax = +8;

% Set up the vector of sample numbers, suitable for making plots

n = Nmin:Nmax;              % A row vector of sample numbers

x = mod(n,N);               % x has the same size as n.  x is also

% full of sample numbers in the fund. period.

for i = 1:length(n),        % Replace the values in x with values

x(i) = xp(x(i)+1);       % from the fundamental period.

end

figure(1);

stem(n, x);

title('Sample Domain -- x(n) vs. n');

xlabel('Sample number, n');

ylabel('x(n)');

% Now find the Discrete-Time Fourier Series of xp

disp('These are the F.S. coeficients');

[ck,k] = dtfs(xp)

ckm = abs(ck);

cka = angle(ck);

figure(2);

stem(k, ckm);

title('Magnitude of ck vs. k');

xlabel('Harmonic number, k');

figure(3);

stem(k, cka);

title('Angle of ck vs. k');

xlabel('Harmonic number, k');

% And finally, synthesize the sample-domain signal from

% the Fourier Series coefficients.

[xs, ns] = dtfs(conj(ck));

xs = abs(N*(xs));

figure(4);

stem(ns, xs);

title('Synthesized fundamental period in sample domain');

xlabel('Sample number, n');

Result of executing file ‘dtfs_ex.m’

» dtfs_ex

These are the F.S. coeficients

ck =

1.0000

-0.5000 + 0.2887i

-0.5000 - 0.2887i

k =

0     1     2

»

Figure 1

Figure 2

Figure 3

Figure 4