Supplementary Information on Program Control Instructions

Supplement to table 11-7 in Mano & Kime 3rd edition.

| Name | Mnemonic | RTL description | Example Comments on the example |
| --- | --- | --- | --- |
| Branch | BR n | PC ( PC + n | BR 05h ; skips 5 addresses ahead BR FBh ; skips back 5 address ; The FBh is twos ; complement for ; –5 base 10) |
| Jump | JMP nn (or JP) | PC ( nn | JMP 1900h ; skips to address 1900h |
| Skip | SKP | PC ( PC + x | SKP ; skips the next instruction |
| Call | CALL nn | (SP) ( PC SP ( SP – 1 PC ( nn | CALL 1900h ; saves return address on ; stack, decrements stack ; pointer, then skips to ; address 1900h |
| Return | RET | SP ( SP + 1 PC ( (SP) | RET ; increment the stack ; pointer, then skip back to ; the return address found ; at the address pointed to ; by the stack pointer. |
| Compare | CMP r (or CP) | ACC – r | CP B ; subtract B from the ; accumulator and set flag ; bits according to the ; result. Does notsave the ; result anywhere. (Only ; affects the flag bits). |
| Test | TEST r r’ or TEST r | r ^ r’ or ACC ^ r | TEST 04h, B ; bitwise AND of the data ; word 04h and data ; stored in register B. Sets ; the flag bits according to ; the result. Does not save ; the result anywhere. (Only affects the flag ; bits.) TEST B ; uses implied addressing ; to do a bitwise AND of ; the accumulator and the ; data stored in register B. ; Otherwise the same as ; above. |

Note: 	n denotes relative addressing mode.
	nn denotes direct addressing mode

r denotes any operand, typically using register or immediate mode addressing

r’ denotes the same as “r” only a different operand